## Slide 1
Smart Watchdog Mechanism for
Real-time Fault Detection in RISC-V
Background
David Simpson
PhD Supervisors:
Prof Jim Harkin
Mr Malachy McElholm
Prof Liam McDaid
Live Demonstration (FPGA)
SNN-based Smart Watchdog
SNN trained to detect control flow errors (CFEs) caused by hardware faults in a RISC-V processor4.
Methodology
8-stages to develop a smart watchdog to monitor a RISC-V processor.
Stage 1 – Data Collection
Faults were injected into the Program Counter register (PC) of RISC-V processor during execution.
Stage 2 – Feature Extraction
Features are extracted from each instruction executed, capturing information on control flow.
Stage 3 – Dataset Preprocessing
Datasets are pre-processed and produced for each of the three applications as shown below.
Stage 4 – SNN Model Design
Stage 7 – Smart Watchdog Implementation
Stage 8 – Smart Watchdog Validation
Stage 5 – SNN Model Training
Stage 6 – SNN Model Testing
Samples | Correct | TP | TN | FN | FP
155 | 152 | 78 | 74 | 3 | 0
Accuracy |  | Precision | Recall | F1 Score | 
0.98 |  | 1.00 | 0.96 | 0.98 | 
Parameter | Value
Network Type | Binary Classifier
Learning Type | Supervised
Development Library | SNNTorch5 (PyTorch)
Epochs | 400
Optimizer | Adam
Batch Size | 1
Loss Function | Mean Square Error
Learning Scheduler Rates | 0.1 / 0.01 / 0.001
Learning Rate Milestones | 10 / 200
Training Dataset: Fibonacci Series
Testing Dataset: Bubble Sort &
Matrix Multiplication
Seen Test Samples at Training: 80/80
(100% accuracy)
Unseen Test Samples During Training: 72/75
(96% accuracy)
Max Freq:
350MHz
Latency: 153 cycles
Inference:
438ns
Validation Dataset: Heap Sort (new application)
Samples | Correct | TP | TN | FN | FP
100 | 98 | 46 | 52 | 2 | 0
Accuracy |  | Precision | Recall | F1 Score | 
0.98 |  | 1.00 | 0.96 | 0.98 | 
New Samples from Heap Sort: 11/11
(100% accuracy)
AMD VC-709 (Virtex-7) FPGA used in this work.
- Lower power consumption
- More hardware friendly
- Smarter watchdog paradigm
Smart Watchdog Aims:
Training and testing datasets are used to develop the SNN model of the smart watchdog.
Total Heap Sort Applications | Applications with Control Flow Errors | Applications with Traps Triggered | Smart Watchdog Detection
1,000 | 840 | 490 (58.3%) | 350 (100%)
RISC-V processor executes a closed-loop PI control algorithm on a DC motor and rotary quadrature encoder.
simpson-d12@ulster.ac.uk
Faults are injected at the program counter register of RISC-V processor.
Instruction data from RISC-V processor was extracted via UART and stored as text files (serial terminal).
Fibonacci Series, Bubble Sort and Matrix Multiplication software applications were executed on RISC-V processor.
Detection mechanisms (watchdogs) must exhibit minimal area overhead and power consumption2.
Spiking Neural Networks (SNNs) could offer a more hardware friendly and efficient implementation3.
Error checking in modern processors is critical1.
See Github page for full details.
School of Computing, Engineering and Intelligent Systems,
Ulster University, Derry, UK
Smart Watchdog Fault Detection Capability
Smart watchdog decisions observed in detail on a custom Python-based GUI.
Builds a library of normal instructions and faulty instructions to train the SNN of the smart watchdog.
Smart watchdog detected all CFEs that were undetected in the RISC-V processor.
Nexys A7-100T development board (AMD Artix-7 FPGA) used as hardware platform for live demonstration.
🚀
Fault Detected (1)
No Fault Detected (0)
IR Opcode 6 (0)
IR Opcode 5 (1)
IR Opcode 4 (2)
IR Opcode 3 (3)
IR Opcode 2 (4)
IR Opcode 1 (5)
IR Opcode 0 (6)
CPU Branched State (7)
CPU Trap Enter State (8)
CPU Trap Exit State (9)
PC Increment (10)
CPU Branch Valid (11)
CPU JAL Valid (12)
CPU JALR Valid (13)
CPU Trap Exit Valid (15)
CPU Trap Entry Valid (14)
Hidden Layer (20)
Output
Layer
(2)
Input
Layer
(16)
Component | FFs | LUTs | Power (W)
Neorv32 | 1,993 | 1,874 | 0.027
Feature Layer | 149 | 157 | 0.001
SNN | 8,928 | 6,494 | 0.142
Smart W-dog | 10,264 | 6,733 | 0.143
Hardware Synthesis Results